## Slide 1: Robust deep reinforcement learning for security and safety in autonomous vehicle systems
Aidin Ferdowsi, Ursula challita, walid saad, Narayan b. mandayam
2018 IEEE international conference on intelligent transportation systems (Itsc)

## Slide 2: Introduction

## Slide 3: Autonomous vehicles in intelligent transportation systems
Autonomous Vehicles (AVs) must process a large volume of data collected by sensors and communication links
This reliance on communications and data processing leaves AVs susceptible to cyber-physical attacks
  Attacker can reduce reliability of measurements by injecting faulty data, possibly inducing accidents
Many security solutions have been proposed for intra-vehicle security (sensors) and inter-vehicle security (communication)
  However, these solutions do not account for the interdependence between the cyber and physical layers of AVs
  Also do not properly model an attacker’s actions and goals
  Does not help to enhance robustness of AV control to attacks

## Slide 4: Paper contributions
Propose a novel adversarial DRL framework to provide robust AV control
  Use “car following” model – control an AV that closely follows another AV
  Use camera, radar, roadside smart sensors (RSS), and inter-vehicle beaconing data from leading car
  Attacker can inject bad data to these sensors
  Goal: optimally control speed while being robust to data injection attacks from attacker

## Slide 5: System model

## Slide 6: Autonomous vehicle cyber-physical system
Each AV must acquire information about own position, speed , and distance and speed of nearby objects
  For car-following model, look at immediately leading AV
Update speed of as function of speed of using
  is estimated speed of AV from AV
  is reaction parameter
Speed estimates come from:
  Camera image
  Radar reading
  Speed report of AV
  Closest RSS reported speed
These are all used to estimate the distance and velocity (complicated Jacobian matrix)

## Slide 7: Attack model
From previous slide, derive  weight matrix and sensor vector
is “under attack sensor vector” – a sensor reading that has faulty data injected into it
, where is injected faulty data and is the sensor vector

## Slide 8: Security problem and game formulation

## Slide 9: Attacker’s goal
Find an attack vector at each time step such that
“Regret function” – quantifies deviation from optimal safe spacing
Distance between AVs
Optimal safe spacing at time t
Basically, trying to find the maximum deviation from the optimal safe spacing

## Slide 10: Defender’s goal
Find a weighting vector to minimize regret function, defined as follows:
, s.t.
These two optimization problems are dependent on the actions of both the attacker and AV
Need to formulate the problem in a game-theoretic framework

## Slide 11: Game theory magic
Lots of theorems and proofs
Ultimately showing that, at each time step, the attacker and defender must choose vectors using past actions
A zero-sum game is defined, which is guaranteed to admit at least one mixed-strategy Nash equilibrium (MSNE) – a stable game state considering all actions of both agents
Though the MSNE exists, it is difficult to derive the equilibrium strategies for each agent  use deep RL algorithm to learn optimal actions

## Slide 12: Adversarial deep reinforcement learning for optimal safe av control

## Slide 13: Proposed rl algorithm
Two components:
  DNN that summarizes past actions and spacing deviations
  RL component, which can be used by each player to decide best action to choose based on summary from DNN
Q-learning algorithm used to select actions
  LSTM blocks used to extract features from continuous state space

## Slide 14: Deep Rl algorithm pseudocode
Used by each player to learn optimal action vectors
Will converge to one of MSNE points of game

## Slide 15: Simulation results, analysis, and conclusion

## Slide 16: Simulation setup and first simulation
Using theorems, found that each AV only needs information about past 6.6 second to carry out optimal safe action
Simulation 1: Attacker can only attack beacon sensor values
Regret reduces to zero after 100 seconds and attacker cannot force AV to deviate from optimal safe spacing
Deviation

## Slide 17: Second simulation
Worst case security scenario: attacker can attack all sensor readings
In first 10 seconds, regret increases abruptly, but stays relatively constant in the remaining time
Since the regret stays approximately constant, defender can feedback the spacing deviation to compensate for deviation from optimal safe spacing

## Slide 18: conclusion
Deep RL method used to enable robust dynamics control for AVs in presence of data injection attacks
LSTM blocks used to extract temporal features from infinite state space to make the RL algorithm work
AV can mitigate effect of data injection attacks on sensor data and stay robust to attacks